## Slide 1: Developments in the security of energy management modules against remote fault injection attacks
Projet ANR JCJC CoPhyTEE
Sécurisation de systèmes sur puce à base d’architecture open-source contre des attaques physiques réalisées à distance basées sur l’énergie
ANR-23-CE39-0003-01
Gwenn Le Gonidec (IETR)
Maria Méndez Real (Lab-STICC, UBS)
Guillaume Bouffard (ANSSI)
Jean-Christophe Prévotet (IETR, INSA Rennes)
owen.le-gonidec@insa-rennes.fr

## Slide 2
Context

## Slide 3
From Secure Elements to Trusted Execution Environments
Secure Element
Simple system
Small attack surface
Complex Systems (SoCs, servers, etc.)
Heterogen, versatile and powerful → Balance between performance, power constraints and security
Large attack surface (software and hardware)
Securing third-party programs
→ Trusted Execution Environments (TEEs) (e.g., Arm Trustzone, Intel SGX)
Many devices and applications rely on TEEs:
Servers (confidential cloud computing)
Applicative SoCs and commodity devices (biometry, DRMs, etc.)
Software-induced hardware attacks emerge from the complexity of the host system.
Hardware attack methods
Software attack → Mass remote exploitation is possible

## Slide 4
Power-management-based attacks

## Slide 5
Power-management-based attacks
Software attacker, high privilege (controls drivers)
Target: trusted application executed on the same applicative multicore CPU
Attacker model
Attack
Through energy management mechanisms, the attacker controls the CPU’s frequency & voltage
→ Clock / Voltage glitch
Reset
Stable
Faults
Re-printed from (1)
1 Mahmoud et al., DFAulted: Analyzing and Exploiting CPU Software Faults Caused by FPGA-Driven Undervolting Attacks, IEEE Access, vol. 10, 2022.
Frequency (MHz)
Voltage (V)

## Slide 6
Energy management mechanisms
DVFS (Dynamic Voltage and Frequency Scaling)
Tang et al., CLKScrew: Exposing the Perils of Security-Oblivious Energy Management, USENIX Security 17, 2017.

## Slide 7
Results
1 Tang et al., CLKSCREW: Exposing the Perils of Security-Oblivious Energy Management, USENIX Security 17, 2017.
2 Qiu et al., VoltJockey: Breaching TrustZone by Software-Controlled Voltage Manipulation over Multi-core Frequencies, AsianHOST, 2019.
3 Noubir et al., Towards Malicious Exploitation of Energy Management Mechanisms, DATE 2020.
4 Murdock et al., Plundervolt: Software-based Fault Injection Attacks against Intel SGX, IEEE Symposium on Security and Privacy (SP), 2020.
5 Kenjar et al., V0LTpwn: Attacking x86 Processor Integrity from Software, USENIX Security 20, 2020.
First attack: CLKScrew (2017)
→ Many similar attacks have been published1—5
  New target platforms
  New attack scenarios
Vulnerable platforms and TEEs
A wide range of Arm Trustzone-based SoCs 1,2
Intel CPUs protected by SGX 4,5 (Skylake)
Compromised security properties
Confidentiality
→ Cipher keys stored in the TEE extracted using DFA1,2,4
Integrity
→ Out-of-Bounds memory access provoked4
Authenticity
→ Forcefully launched ill-signed programs in the TEE1,2
Availability
→ Denial-of-Service attacks3
Main fault model: The result of some operations is faulted (multiplications, vector operations, encryption)

## Slide 8
Limits of DVFS attacks
Re-printed from: Juffinger et al., SUIT: Secure Undervolting with Instruction Traps, 29th ACM International Conference on Architectural Support for Programming Languages and Operating Systems, 2024
Voltage regulators can be imprecise
Timing accuracy
Notes: (SUIT: the CPU is an Intel Core i9-9900K)

## Slide 9
Potential evolutions
Power management hardware evolution
Combination with other attacks
New ways to manipulate voltage and frequency
Notes: Some data. SUIT (2024): 335us (Intel Xeon), 668us (AMD Ryzen 7)

## Slide 10
Countermeasures

## Slide 11
Approaches to countering DVFS attacks
Prevent malicious use of power management mechanisms by the attacker
Strengthen the hardware against voltage & frequency variations
Make trusted programs robust against fault attacks

## Slide 12
DVFS attacks countermeasures — First approach
→ Intel/Arm approach: prevent software from accessing voltage regulators
Impact on power management mechanisms?
Other ways to manipulate voltage (e.g. FPGA-to-CPU attack)
→ Use of a coprocessor to control voltage/frequency change requests
Cost and energy consumption of the component
Zhang et al., Blacklist Core: Machine-Learning Based Dynamic Operating-Performance-Point Blacklisting for Mitigating Power-Management Security Attacks, ISLPED '18: International Symposium on Low Power Electronics and Design, 2018

## Slide 13
DVFS attacks countermeasures — Second approach
Juffinger et al., SUIT: Secure Undervolting with Instruction Traps, 29th ACM International Conference on Architectural Support for Programming Languages and Operating Systems, 2024
→ Increase the latency of frequently faulted instructions
Requires hardware modifications to the CPU
Impact on performances
Re-printed from Liang et al., ReVIVaL: A Variation-Tolerant Architecture Using Voltage Interpolation and Variable Latency, 2008 International Symposium on Computer Architecture

## Slide 14
DVFS attacks countermeasures — Third approach
→ Well-known methods: redundancy, infection, error detection codes, etc.1
→ Identify vulnerable code sections2
→ Insert new instructions to protect against attacks3
Heavy impact on performances
Useful against other fault injection attacks
1 Tao et al., Software Countermeasures against DVFS fault Attack for AES, 10th International Conference on Dependable Systems and Their Applications (DSA), 2023.
2 Zhang et al., iATPG: Instruction-level Automatic Test Program Generation for Vulnerabilities under DVFS attack, IEEE 25th International Symposium on On-Line Testing and Robust System Design (IOLTS), 2019
3 Kogler et al., Mineﬁeld: A Software-only Protection for SGX Enclaves against DVFS Attacks, 31st USENIX Security Symposium (USENIX Security 22), 2023

## Slide 15
Conclusions

## Slide 16
Conclusions
Prospects for countermeasures
  Arm Trustzone, Intel SGX: limited and specific countermeasures
Survey article
Do not Trust Power Management: A Survey on Internal Energy-based Attacks Circumventing Trusted Execution Environments Security Properties
(Pre-print available on arXiV:
https://doi.org/10.48550/arXiv.2405.15537)
DVFS attacks: an important threat
  Wide range of vulnerable applications and devices
  Software attack → remote and mass exploitation
  Many possible evolutions → Impact of the evolution of power management mechanisms on the attack surface? → What are the other ways to control voltage & frequency?
  → How to design TEE implementations that are fundamentally secure against software-induced hardware attacks?
  RISC-V TEEs are an opportunity
Thanks for your attention!